A Checklist for the Design of Extra Care Housing

Typical Schedule of Accommodation

The following schedule represents a scheme of 50 flats and gives an indication of spaces to consider with suggested floor areas. Project specific factors will dictate which spaces are appropriate and where they are located within the scheme. For example some schemes will offer formal day care and will, therefore, be able to sustain more activity spaces and there will be different requirements in schemes located in vibrant urban settings as opposed to a quiet rural area.

| Accommodation | Approximate Area |
| --- | --- |
| RESIDENTS ACCOMMODATION |  |
| 34 No. 1-Bed 2-Person Flats (See Typical Layout in Appendix). 16 No. 2-Bed 3-Person Flats (See Typical Layout in Appendix). | 51 sq metres 68 sq metres |
| COMMUNAL ACCOMMODATION & FACILITIES |  |
| Main communal lounge Located near to and visible from the main entrance with a focal point such as a fireplace or similar. Dining and lounge spaces should be linked but should occupy distinctly separate spaces. Views and direct access onto a south facing terrace and garden are a major benefit. Alcoves and niches will allow smaller groups to gather together. | 1.5 sq metres per resident |
| Dining area If possible this room should link to an external terrace to allow dining outside in good weather. This space could be designed in several ways, as a restaurant or café with table service or servery counter, or as a domestic dining room. Allow space for residents using wheelchairs and walking aids. | 1.2 sq metres per resident or 2 sq metres per diner |
| Residents tea kitchen Provide adjacent to lounge and dining space, for use by residents and for refreshments for small functions. Could double up as servery counter for main meals. | 10 sq metres |
| Small lounges or hobby rooms (2 minimum) Can be located on upper floors and used for private parties with relatives, small gatherings, specific activities etc. Should be easily accessible and not located at the ends of corridors or isolated from the main circulation route. The number of these will depend on the size of the scheme and whether the flats are arranged in clusters. | Min 15 sq metres each |
| Communal WCs Located near to entrance area and communal lounge/dining areas. Designed for wheelchair accessibility. | 4 sq metres each |
| Assisted bathrooms (2 minimum) At least 1 per floor, equipped with baths to allow both assisted and independent use by residents. These rooms should be designed to be as domestic as possible, space should allow baths to be located in a peninsula position. | 12 – 15 sq metres |
| Hairdressing & Beauty Therapy Could be located near to entrance area and might have a multi-purpose use. | Min 12 sq metres |

| Accommodation | Approximate Area |
| --- | --- |
| Informal seating spaces Beside main entrance, along corridors and at ends of corridors. Number will be dependant on the individual scheme layout. | Min 3 sq metres each |
| STAFF & ANCILLARY ACCOMMODATION |  |
| Manager’s office With views into the main entrance area, space for desk, computer table, chair, plus two visitors chairs and document storage. | Min 12 sq metres 15m_ minimum |
| Care Staff office Space for two desks, files storage and table for handover meetings. Privacy is important due to the confidential nature of the work. | Min 15 sq metres |
| Photocopy area Easily accessible by all staff. | 4 sq metres |
| Staff overnight room with en-suite facilities The need for this space will depend on staff arrangements and whether night waking staff will be employed. | 18 sq metres |
| Staff rest room with kitchenette Space for table and chairs plus a couple of armchairs. It may be worth considering a staff smoking area e.g. a covered external terrace. | Min 15 sq metres |
| Staff locker/change room & WC All staff will need locker space and possibly an area for changing clothes. Provide at least two dedicated staff toilets and consider the need for a separate staff shower. | 10 sq metres |
| Guest room with en-suite To be designed for wheelchair user access, accommodating two twin beds with en-suite shower, WC and basin. | 20 sq metres |
| Laundry For use by residents and staff with adjoining external drying yard. It may be appropriate to divide the laundry to provide separate resident and staff areas. | 30 sq metres |
| Sluice room Consider the need for this facility which could be incorporated into the main laundry. | 5 sq metres |
| Main catering kitchen and associated storage and staff facilities The brief for this space will depend on whether a full catering service is to be provided or if the requirement is for a less intensive use e.g. regeneration kitchen. | 55 sq metres |
| Cleaners storage | 5 sq metres each |
| General storage | Min 15 sq metres |
| Large re-charging store for electric buggies and scooters | 25 – 30 sq metres |
| Public payphone Consider whether this is required as most residents will have access to their own private telephones. |  |

| Accommodation | Approximate Area |
| --- | --- |
| SERVICES & PLANT |  |
| Minimum of 1 no. Lift to all floors: minimum 13 person (stretcher size). | 2600 x 1800mm shaft approx |
| Lift Motor Room if required | 4 sq metres |
| Refuse store (including lobby and cupboard for Clinical waste). | 16 sq metres |
| Recycling collection point | 6 sq metres |
| Plant room & service risers The size of plant room(s) will vary significantly from scheme to scheme depending on the method of space heating selected and the extent of individual metering decided upon. Space required for water storage (including the possibility of booster tanks and pumps if the building height dictates) will also vary. As a guide allow 20-25m_, but ensure specialist service engineer’s advice on size and location at the earliest possible opportunity. |  |
| Electrical intake/meter room | 10 sq metres |

Other spaces to consider

A number of additional spaces should be considered which will of course be determined by factors specific to the site, the scale of development and local need. The need for such additional facilities may be identifiable but it may still be financially prohibitive. Where appropriate consider the following additional facilities:

Shop.

Library.

Therapy Suite.

Treatment Rooms.

IT Facilities/Information Points/Touch Screens.

Café/Bar/Pub.

Leisure Facilities.

Outreach staff offices.

External areas

In addition to the brief guidance on garden design given in Section 5 the following should be considered:

Adequate Car Parking for residents, visitors, staff and visiting professionals, including disabled parking bays.

Requirements for minibus drop-off under cover. To allow for the anticipated size of such vehicles.

Emergency and service vehicles – turning heads and waiting bays.

Maintenance/Garden store.

Bicycle store.

Refuse, clinical waste and recycling storage.